## Slide 1: ROS + Gazebo Quadcopter Simulator

## Slide 2: What is ROS?
ROS is an open-source robot operating system
A set of software libraries and tools that help you build robot applications that work across a wide variety of robotic platforms
ROS topics are named communication buses that exchange messages between ros nodes and have anonymous publish/subscribe semantics
Several robotics sensors that are supported by official ROS packages
topics
algorithms
sensors
controllers

## Slide 3: What is Gazebo?
A simulator for robot research
  Real time physic engine
  High-quality graphics (ORGE)
  A rich set of Sensor & Plugins

## Slide 4
Simulated Drone Framework (ROS-GAZEBO)
/drone/cmd_val
/drone/land /drone/posctrl /drone/reset /drone/takeoff
/drone/imu
/image_raw
lib_plugin_ros_init.so
lib_plugin_drone.so
lib_plugin_ros_imu.so
lib_plugin_ros_cam.so
Gazebo
ROS Environment
ROS-Gazebo Integration
Gazebo Environment

## Slide 5: Contd...!
lib_plugin_ros_init.so
  A system plugin for gazebo server
lib_plugin_ros_drone.so
  Receives commands from 'drone_keyboard’ through ROS topics
  A simple pid controller for inner-loop
  A simple position controller
lib_plugin_ros_imu.so
  It’s sensor plugin, Publishes the imu(Inertial Measurement Unit) data to ROS.
lib_plugin_ros_cam.so
  It’s sensor plugin, Publish the image data to ROS topics

## Slide 6: Simulated Drone Activity Diagram

## Slide 7: Results: Sample Screenshots
Simulated drone flying in Agriculture terrain
Drone down camera captured Agriculture terrain imges

## Slide 8: Terrain Orthomosaic Map
The collected terrain Images parsed with ODM software to generate terrain Point cloud, 2D, 3D Orthophotos, Reporting.
Web ODM is the processing engine, whicsh can be used from the command line. It takes images as input and produces a variety of outputs, including point clouds, 3D models and orthophotos